 Find the measurements requested for the waveform shown below.

# Find the period of this repetitive waveform.
T = ________ ___
# Find the frequency of this repetitive waveform.
f = ________ ___
# Find the pulse amplitude for the waveform.
PA = ________ ___
# On the graph above show how to measure the pulse width of the waveform and record the value here.
PW = ________ ___
# On the graph above show how to measure the rise time tr and the fall time tf of the waveform, and record the values here.
tr = ________ ___
tf = ________ ___
# Find the duty cycle for the waveform.
duty cycle = ________
# Which waveforms contain harmonic frequencies?
## only sine waves
## only square waves
## all waveforms including sine waves
## all waveforms except sine waves
____
# Poorly adjusted RF amplifiers often produce second harmonics which may then be broadcast. If a trucker uses a poorly adjusted CB radio on 27 MHz, what will the frequency of the second harmonic be?
f(2nd) = ________
# The specifications for an amplifier indicate that the power gain of an amplifier is 150,000. What is the decibel power gain of the amplifier?
Ap (dB) = ________
# The input voltage to an amplifier is 10 millivolt and the output voltage is 1.2 Volts. What is the decibel voltage gain of the amplifier?
Av (dB) = ________
# Assume a certain amount of power is attenuated by - 10dB. If the input power to the attenuator is 1 watt, what is the output power?
POUT = __________
# Calculate the upper cutoff frequency f2 of the circuit below.
f2 = __________
# If the input voltage to the circuit above is 100 volts and the frequency of the input is equal to the upper cutoff frequency f2 what is the output voltage?
VO __________

# A differential circuit amplifies
## only AC.
## only DC.
## both AC and DC.
## neither AC nor DC.
_____
# The voltage difference between the inputs of a differential amplifier needed to give a zero output voltage is called the
## input offset current
## input bias current
## output impedance
## input offset voltage
_____
# A differential amplifier has a gain of 100 when a difference signal is applied, and a gain of 0.2 when a common-mode signal is applied to both inputs. Calculate the CMRR as a ratio and in dB. Show your calculations.
CMRR = __________
CMRR (dB) = __________
_____
# When an op amp is operated without feedback is it said to be operating
## derated.
## compensated
## open-loop.
## closed-loop.
_____
# The waveform shown below is the output of an op-amp with a (perfect) pulse input. What is the slew rate of the amplifier?
slew rate = __________ volts/s
# When any waveform exceeds the slew rate of the op amp,
## the op amp works best.
## the voltage gain is maximum.
## linear operation occurs.
## distortion occurs.
_____
# Assume a saturation voltage of ±14 volts for a 741 op amp. If the open loop gain for the op amp is 200,000, what differential input voltage VIN = (VIN+ - VIN-) will be required to cause the output to just saturate?
VIN = __________
# Adding negative feedback to an amplifier
## increases the input and output impedances.
## increases the input impedance and decreases the output impedance.
## decreases the input impedance and increases the output impedance.
## decreases the input and output impedances.
_____
# The use of negative feedback
## reduces the voltage gain of an amplifier from its open-loop value.
## increases the voltage gain of an amplifier from its open-loop value.
## has no effect on the voltage gain of the amplifier.
## can either increase or decrease the voltage gain of the amplifier from its open-loop value.
_____
# A non-inverting amplifier circuit has a closed-loop gain of 25. The op-amp by itself has an open-loop gain of 100,000. If a new op-amp with an open-loop gain of 200,000 is substituted in the circuit, the circuit closed-loop gain will
## decrease by a factor of 2.
## increase by a factor of 25.
## increase by a factor of 2.
## change very little.
_____
# Draw the circuit for an inverting amplifier. Give each resistor a label, and label the input and output connections.

-
+

# Write the formula for the voltage gain of the inverting amplifier in terms of the resistor labels you used in the previous question.

# Draw the circuit for a non-inverting amplifier. Give each resistor a label, and label the input and output connections.

-
+

# Choose resistors for the non-inverting amplifier circuit above so that an AC input voltage of 150 millivolts peak-to-peak will produce an output voltage of 1.0 volt p-p. Mark the resistor values on the drawing above. Show your calculations below.

# Compensation prevents an amplifier from oscillating. What is the disadvantage of fully compensating an amplifier?
## reduced bandwidth
## increased oscillation amplitude
## reduced phase margin
## reduced positional notation
_____
# The boxes shown below contain amplifiers. The input and output waveform of each is shown. Which of the amplifiers is a linear amplifier ?

_____
# How many output voltage levels can a 14-bit D/A converter produce?
__________ levels

# An input transducer converts
## voltage to current.
## current to voltage.
## a non-electrical quantity to an electrical quantity.
## an electrical quantity to a non-electrical quantity.
_____
# In electronic circuits the term rail refers to _____________________________________.

# In electronic circuits the term rail to rail refers to _____________________________________.

# Define Transducer:

# The TI SN754410 Quadruple HALF H DRIVER is a:
_____
## Logic
## Linear
## Mixed Signal
## Transmitter
# An LM35 is a:
_____
## Logic
## Linear
## Mixed Signal
## Transmitter
# A junction between two different metals that produces a voltage related to a temperature difference.

## Thermal Coupler
## Thermal Coupling
## RTD
## Thermocouple
_____
# A system which uses 4-20mA might be called a: _____________
## Current Loop
## Eddy Current
## Transducer
## Transmitter
# Calculate the output voltage from the binary-weighted summing amplifier shown below.
VO = __________
# List the five basic types of filter responses:
##
##
##
##

# Attenuation refers to:
## a loss of signal strength.
## a constant signal.
## a gain of signal strength.
## Phase shift in the signal.
_____
# The order of a filter is
## the number of inductors and capacitors in the filter.
## the number of resistors in the filter.
## the number of operational amplifiers or transistors in the filter.
## the number of ripples in the passband or stopband.
_____
# The world's loudest band, is:
## Metallica
## Spin̈al Tap
## Cradle of Filth
## Herb Alpert & the Tijuana Brass
_____
# A filter is designed to filter out 60 Hz from a guitar amplifier, but to allow other frequencies above and below 60 Hz to be amplified. This would be a
## low-pass filter.
## band-pass filter.
## high-pass filter.
## band-stop filter.
_____
# The filter shown below is a
## first-order high-pass filter.
## first-order low-pass filter.
## second-order high-pass filter.
## second-order low-pass filter.
## Mrs. Butterworth's
_____
# A comparator typically has
## an analog input voltage and an analog output voltage.
## an analog input voltage and a digital output voltage.
## a digital input voltage and a digital output voltage.
## a digital input voltage and an analog output voltage.
_____
# A Schmitt trigger is a comparator with ___________________ and ____________________.

# Using the following schematic and output plots, label each plot with its node name (A,B,C, and D).

# Using the above schematic and output plots, indicate what type of circuit you see (the common name) for the nodes A,B,C, and D.
# A. ________________________________________

# B. ________________________________________

C. ________________________________________
D. ________________________________________
# An oscillator differs from an amplifier because
## it requires no dc supply voltage to make an output signal.
## it always has a higher gain.
## it requires no input signal to make an output signal.
## it has an inverted output signal.
_____
# One condition for oscillation in any feedback oscillator is that the amplifier and the feedback network together have a phase shift of
## 180.
## one-fifth (1/5).
## five.
## 0 (or 360)
_____
# Another condition for oscillation in any feedback oscillator is that the total gain of the amplifier and the feedback loop must be at least
## zero.
## one-fifth.
## one.
## three.
_____
# An astable multivibrator
## provides a time-delay dependent on the input pulse width.
## oscillates when supplied with only DC power.
## puts out a fixed-width pulse each time it is triggered.
## rejects all frequencies except one frequency.
_____
# A monostable multivibrator is also called a
## flip-flop.
## oscillator.
## single-frequency filter.
## one-shot.
_____